## Slide 1
3rd IEEE International Conference on
Artificial Intelligence for Internet of Things
AIIoT 2024
03 - 04, May 2024
LoRa-Enabled NodeMCU Nodes for Efficient Agricultural Monitoring in IoT: Integration with Raspberry Pi Web Application
Prachi Sharma, Associate Professor, Vellore Institute of technology, VIT Vellore, India. prachi.sharma@vit.ac.in
Parshwanath V Jain, Student, Vellore Institute of technology, VIT Vellore, India. parshwanath.2021@vitstudent.ac.in
Dhruv Akar, Student, Vellore Institute of technology, VIT Vellore, India. dhruv.akar2021@vitstudent.ac.in
Ahzam Afaq, Student, Vellore Institute of technology, VIT Vellore, India. ahzam.afaq2021@vitstudent.ac.in
Paper ID: 1672

## Slide 2: Agenda
Abstract
Introduction
Literature Survey
Proposed Methodology
Results
Conclusion
References

## Slide 3: Abstract
Agricultural monitoring is essential for optimizing crop production and ensuring food security. However, conventional methods of monitoring are often costly, labor intensive, and unreliable. In this paper, we propose a novel agricultural monitoring system that uses a network of low-cost, low-power, and long-range devices to collect and transmit data on various soil and environmental parameters. The system consists of a main central unit based on Raspberry Pi, and several nodes distributed across the field, each equipped with an ESP32 microcontroller and sensors for measuring soil moisture, water level, temperature, and humidity. The nodes communicate with the central unit using LoRa, a wireless technology that offers long range, low-bandwidth, and low-power communication. We compare the performance of LoRa with other wireless technologies such as Wi-Fi and ZigBee and show that LoRa has several advantages in terms of range, power consumption, scalability, and robustness. The central unit processes the data and displays it on a web interface, which allows the user to monitor the field conditions and control the irrigation system remotely. We evaluate the feasibility and effectiveness of our system through simulations and experiments, and demonstrate that it can provide accurate, timely, and reliable information for agricultural management.

## Slide 4: Introduction
Agriculture: Pillar of civilization, ensuring sustenance and economic stability worldwide.
Evolution: Incorporating technology to enhance productivity, sustainability, and efficiency.
Challenges: Traditional methods costly, time-consuming, and prone to errors.
Solution: Leveraging IoT and LoRa technology for efficient agricultural monitoring.

## Slide 5: Introduction
Components: ESP32 microcontrollers and LoRa-enabled NodeMCU nodes for data collection.
Central Unit: Raspberry Pi platform orchestrates data aggregation, processing, and dissemination.
Advantages of LoRa: Extended range, low-power consumption, scalability, and robustness.
User-Centric Design: Web-based interface for real-time field data access and control functionalities.
Conclusion: A scalable, cost-effective, and reliable solution for sustainable agricultural monitoring.

## Slide 6: Literature Survey
IoT applications - analyze data, forecast future conditions, enhancing productivity, reducing costs and preserving resources.
Agricultural Monitoring System uses a network of low-cost, low-power and long-range devices to collect and transmit data on various environmental parameters like soil moisture, water level, temperature and humidity.
Nodes (ESP32 microcontrollers) communicate with central unit using LORA which provides long-range, low-bandwidth and low-power communication.
Main Central Unit - Raspberry pi platform - data aggregation, processing and dissemination.

## Slide 7: Literature Survey
Web based interface - ThingSpeak server - monitor field conditions remotely and make informed decisions regarding irrigation management and crop cultivation practices.
LoRa:
1. Superior penetration through obstacles like cement and reinforced concrete walls, providing longer communication distances.
2. Lower RTT (Round Trip Times)
3. Ideal for precision agriculture, offering long range communication with low power consumption.
ZigBee:
1. Supports long distance communication through routing nodes.
2. Faces challenges with data packet loss.
3. Viable option considering cost and power consumption.

## Slide 8: Proposed Methodology
The main part is to set up the main Raspberry Pi structure and then to integrate the ESP32 as a node receiver and then to finally send and execute the commands required.
The major steps are listed below:
1. Raspberry Pi setup as a server and central node and command center for the entire field.
2. ESP32 is set up with LoRa receiver to receive commands and also send feedback about the status of the node.

## Slide 9: Proposed Methodology
3. LoRa communication network is set up to send and receive information.
4. All sensor units of Soil moisture, Rainfall, Humidity and temperature along with the motor and LED are also set up to monitor the status of the nodes at which they are present thus giving the overall view of the entire field.

## Slide 10: Results
Upon the successful implementation of our system, we observed the transmission of data to the ThingSpeak server. The outcomes pertaining to LoRa technology were particularly noteworthy, as the Received Signal Strength Indication (RSSI) values were meticulously recorded for each transmission. Notably, the RSSI values exhibited a quadratic decline with increasing distance, a phenomenon indicative of signal attenuation over distance.
The RSSI values provided in decibels (dB) serve as crucial metrics, reflecting the signal strength of individual data transfers. This parameter is directly associated with the quality of data transmission and the spatial proximity of the nodes to the central server.

## Slide 11: Results
The observed trends in RSSI values not only affirm the efficacy of the LoRa technology but also underscore. its potential in enabling robust and efficient communication across varying distances within the agricultural monitoring network.

## Slide 12: Conclusion
In brief, our research introduces an innovative agricultural monitoring approach using emerging IoT technologies, particularly LoRa, to overcome conventional method limitations.
Through a network of low-cost, low-power LoRa devices, we've demonstrated the feasibility and effectiveness of our system, highlighting LoRa's advantages in range, efficiency, scalability, and reliability, crucial for remote environments.
Our system integrates ESP32-based nodes with various sensors for real-time soil monitoring, managed by a Raspberry Pi central unit, enabling intuitive data collection and analysis.
Thorough evaluations confirm the system's capability to provide accurate, timely information, enhancing agricultural management, operational efficiency, and food security efforts.

## Slide 13: References
[1] J. Haxhibeqiri, E. De Poorter, I. Moerman, and J. Hoebeke, “A Survey of LoRaWAN for IoT: From Technology to Application,” Sensors (Basel)., vol. 18, no. 11, 2018.
[2] A. Khanna and S. Kaur, “Evolution of Internet of Things (IoT) and its significant impact in the field of Precision Agriculture,” Comput. Electron. Agric., vol. 157, no. November 2018, pp. 218–231, 019.
[3] Ahmed, Mohamed A., Jose Luis Gallardo, Marcos D. Zuniga, Manuel A. Pedraza, Gonzalo Carvajal, Nicolás Jara, and Rodrigo Carvajal. 2022. "LoRa Based IoT Platform for Remote Monitoring of Large-Scale Agriculture Farms in Chile" Sensors 22, no. 8: 2824. https://doi.org/10.3390/s22082824J
[4] Swain, M., Zimon, D., Singh, R., Hashmi, M. F., Rashid, M., & Hakak, S. (2021). LoRa-LBO: An experimental analysis of lora link budget optimization in custom build iot test bed for agriculture 4.0. Agronomy, 11(5). https://doi.org/10.3390/agronomy11050820
[5] Zhu, M., & Shang, J. (2022). Remote Monitoring and Management System of Intelligent Agriculture under the Internet of Things and Deep Learning. Wireless Communications and Mobile Computing, 2022. https://doi.org/10.1155/2022/1206677
[6] Suji Prasad, S. J., Thangatamilan, M., Suresh, M., Panchal, H., Rajan, C. A., Sagana, C., Gunapriya, B., Sharma, A., Panchal, T., & Sadasivuni, K. K. (2022). An efficient LoRa-based smart agriculture management and monitoring system using wireless sensor networks. International Journal of Ambient Energy, 43(1), 5447–5450. https://doi.org/10.1080/01430750.2021.1953591

## Slide 14: References
[7] Yascaribay, Geovanny, Mónica Huerta, Miguel Silva, and Roger Clotet. 2022. "Performance Evaluation of Communication Systems Used for Internet of Things in Agriculture" Agriculture 12, no. 6: 786. https://doi.org/10.3390/agriculture12060786.
[8] Liu, Z., Li, Y., Zhao, L., Liang, R., & Wang, P. (2022). Comparative Evaluation of the Performance of ZigBee and LoRa Wireless Networks in Building Environment. Electronics (Switzerland), 11(21). https://doi.org/10.3390/electronics11213560
[9] Miles, B., Bourennane, E.B., Boucherkha, S., Chikhi, S.: A study of LoRaWAN protocol performance for IoT applications in smart agriculture. Comput. Commun. 164, 148–157 (2020)
[10] Prakosa, S.W., Faisal, M., Adhitya, Y., Leu, J.S., Köppen, M., Avian, .: Design and implementation of LoRa based IoT scheme for Indonesian rural area. Electronics 10(1), 77 (2021). https://doi.org/10.3390/electronics10010077
[11] H. Klaina et al., “Analysis of low power wide area network wireless technologies in smart agriculture for large-scale farm monitoring and tractor communications,” Measurement, vol. 187, Jan. 2022, Art. no.110231.
[12] S. Sendra, L. García, J. Lloret, I. Bosch, and R. Vega-Rodríguez, “LoRaWAN network for fire monitoring in rural environments,” Electronics, vol. 9, no. 3, p. 531, 2020.
[13] R. El Chall, S. Lahoud, and M. El Helou, “LoRaWAN network: Radio propagation models and performance evaluation in various environments in lebanon,” IEEE Internet Things J., vol. 6, no. 2, pp. 2366–2378, Apr. 2019.
[14] Ray, B., Islam, N., & Biplob Ray, nd. (n.d.). IoT Based Smart Farming: Are the LPWAN Technologies Suitable for Remote Communication? https://www.researchgate.net/publication/344